## Slide 1
Chapter 4
Circuit Theorems
EBN 111/122 ELECTRICITY AND ELECTRONICS

## Slide 2: Circuit Theorems - Chapter 4
4.1 Motivation
4.2 Linearity Property
4.3 Superposition
4.4 Source Transformation
4.5 Thevenin’s Theorem
4.6 Norton’s Theorem
4.8 Maximum Power Transfer

## Slide 3: If you are given the following circuit, are there any other alternative(s) to determine the voltage across 2W resistor?
What are they? And how?
Can you work it out by inspection?
4.1 Motivation

## Slide 4: 4.2 Linearity Property
It is the property of an element describing a linear relationship between cause and effect.
A linear circuit is one whose output is linearly related (or directly proportional) to its input.
Two properties of linearity
Homogeneity (scaling)
v = i R → k v = k i R
Additivity
v1 = i1 R and v2 = i2 R
→ v = (i1 + i2) R = v1 + v2
Assume vs = 10V ⟹ i = 2 A
then: vs = 1V ⟹ i = 0.2 A
vs = 100V ⟹ i = 20 A

## Slide 5
Example 4.2 Assume Io = 1 A and use linearity to find the actual value of Io in the circuit.
If Io = 1 A: V1 = 1(3+5) = 8 V.
With V1 = 8 V: I1 = 8/4 = 2 A.
With I1 = 2 A: I2 = Io + I1 = 1+2 = 3 A (KCL)
With I2 = 3 A: V2 = V1 + I22 = 8+6 = 14 V
With V2 = 14 V: I3 = 14/7 = 2 A
With I3 = 2 A: I4 = I2+ I3 = 3 + 2 = 5 A (KCL)
Thus: Io/I4 = Io/IS = 1/5 A.
Due to linearity: Io_actual = 1/5 * IS_actual = 3 A

## Slide 6
PP 4.2 Assuming Vo = 1 V, use linearity to calculate the actual value of Vo.
Assume Vo = 1 V:
  From voltage division:
  Hence: Vo = 2.5 V.
Thus: (This relationship will always be true for this circuit.)
If V1 is equal 30 V, then according to linearity principle:
V0 = 0.4 V1 = 12 V
V1
i

## Slide 7: 4.3 Superposition Theorem
The voltage across (or current through) an element in a linear circuit is the algebraic sum of the voltage across (or currents through) that element due to EACH independent source acting alone.
The principle of superposition helps us to analyze a linear circuit with more than one independent source by calculating the contribution of each independent source separately.

## Slide 8: 4.3 Superposition Theorem
We consider the effects of 8A and 20V one by one, then add the two effects together for final vo.

## Slide 9: 4.3 Superposition Theorem STEPS
Steps to apply superposition principle
Turn off all independent sources except one source. Find the output (voltage or current) due to that active source using nodal or mesh analysis.
Repeat step 1 for each of the other independent sources.
Find the total contribution by adding algebraically all the contributions due to the independent sources.

## Slide 10: 4.3 Superposition Theorem Zeroing of Sources
How do you turn off a source, i.e. make it zero?
Independent sources:
  Independent voltage sources are replaced by 0 V (short circuit (R=0 ))
  Independent current sources are replaced by 0 A (open circuit (R   )).
Dependent sources are left intact because they are controlled by circuit variables.

## Slide 11
PP 4.5:
Use superposition
to find I.
Switch off the 4 A and 12 V sources:
Switch off the 4 A and 16 V sources:
Switch off the 12 V and 16 V sources:
I1 = 16/16 = 1 A
I2 = - 12/16 = -0.75 A
I3 = 4 [2 / (2 + 14)] = 0.5 A
I = I1 + I2 + I3
= 1 + -0.75 + 0.5
= 0.75 A

## Slide 12
PP 4.4:
Use superposition
to find vx.
Switch off (zero) the 4 A source:
Switch off (zero) the 20 V source:
Nodal-analysis:
Nodal-analysis:
Total: vx = vx1 + vx2 = 5 + 20 = 25 V

## Slide 13
An equivalent circuit is one whose v-i characteristics are identical with the original circuit.
It is the process of replacing a voltage source VS in series with a resistor R by a current source IS in parallel with a resistor R, or vice versa.
Ch. 4 L#2:
4.4 Source Transformations

## Slide 14: 4.4 Source Transformation
(a) Independent source transform
(b) Dependent source transform
The arrow of the current source is directed toward the positive terminal of the voltage source.
The source transformation is not possible when R = 0 for voltage source and R = ∞ for current source.
+
+
+
+
-
-
-
-

## Slide 15: 4.4 Source Transformation From a Load’s perspective
A load connected between terminals a-b will not know the difference. The load will see the same voltage and conduct the same current.
+
+
-
-
Load
Load

## Slide 16
PP 4.5: Use source transformation and determine io.
5 V
5 A
3 A
6//3 = 2 
1+4= 5 
7 
io
5  2 = 10 V
2 
7 
io
3 A
5 
5 V
7 
3 A
5 
5 + 10 = 15V
2 
io
7 
3 A
5 
io
2 
15/2= 7.5 A
7.5+3=
10.5 A
7 
io
5//2 = 

## Slide 17
PP 4.5b: Use nodal analysis and determine io.
KCL @ Supernode:
2
Supernode:
1
x30
V1
V2

## Slide 18
PP 4.7: Use source transformation and determine ix.
Very IMPORTANT:
Do NOT transform the part of the circuit with the unknown variable!

## Slide 19
Problem 4.24: Determine vx.

## Slide 20
It states that a linear 2-terminal circuit (Fig. a) can be replaced by an equivalent circuit (Fig. b) consisting of a voltage source VTH in series with a resistor RTH,
where
VTH is the open-circuit voltage (Voc) at the terminals.
RTH is the input or equivalent resistance at the terminals when the independent sources are turned off.
Ch. 4 L#3:
4.5 Thevenin’s Theorem

## Slide 21
4.5 Thevenin’s Theorem How to determine Vth and Rth
To determine Vth:
Voc = Vth
Voc = Open Circuit Voltage.
Terminals a-b are terminals between which you want to determine the Thevenin equivalent.
Can be anywhere in the circuit.
To determine Rth:
Method #1:
Zeroing of Sources:
If the circuit contains no dependent sources.

## Slide 22
4.5 Thevenin’s Theorem How to determine Rth Case 2
Test Sources
Method #2: Application of test sources, if the circuit does contain dependent sources.
MUCHO IMPORTANTE:
You cannot turn off dependent sources as they are controlled by circuit variables.

## Slide 23
PP 4-8:
Determine the Thevenin equivalent circuit to the left of terminals a-b.
Determine I.
V1
x30:
Rth: Zero Ind. Sources:
Rth = 4//(6+6) = 3 
9 V
3 
I = 9/4
=2.25 A
For I:
Vth: Calculate Voc = Vab:

## Slide 24
PP 4-9:
Determine the Thevenin equivalent circuit to the left of terminals a-b.
V1
Vth: Calculate Voc = Vab:
x35:

## Slide 25
PP 4-9: continued
Rth: Method A
Rth: Zero Ind. Sources + CURRENT Test Source: Need Vab = Vo
1 A
Vx
Vo
x15:
1
x12:
2
+ 8x :
2
1

## Slide 26
PP 4-9: continued
Rth: Method B
Rth: Zero Ind. Sources + VOLTAGE Test Source: Need io
io
Vx
x15:
x12:
KCL:

## Slide 27
Problem 4-39:
Determine the Thevenin equivalent circuit.
Vth: Calculate Voc = Vab
Vab = V5 + V16:
+
V5
_
- V16 +
i1
i2
Loop 2: i2 = -1 A
Loop 1:
-8 + 10i1 +10(i1 – i2) + 5i1 = 0
25i1 = -2
i1 = -0.08 A
Vth = V5 + V16
= 5i1 + 16i2
= 5(-0.08) + 16(-1)
= -16.4 V
Rth: Zero Ind. Sources:
Rth = 16+ 5//(10+10)
= 20 
+
Vab
_

## Slide 28
It states that a linear two-terminal circuit can be replaced by an equivalent circuit of a current source IN in parallel with a resistor RN,
Where
IN is the short circuit current through
the terminals.
RN is the input or equivalent resistance
at the terminals when the independent
sources are turned off.
Ch. 4 L#4:
4.6 Norton’s Theorem

## Slide 29
4.6 Norton’s Theorem Norton vs Thevenin
Where:
RN = Rth
IN = Vth/Rth = Vth/RN
Vth = INRth = INRN
Norton equivalent = Source transformation of the Thevenin equivalent and vice versa.

## Slide 30
4.6 Norton’s Theorem How to determine IN and RN
To determine IN:
isc = short circuit current.
Terminals a-b are terminals between which you want to determine the Norton equivalent.
Can be anywhere in the circuit.
To determine RN:
Methods #1 and #2 as with Rth since RN = Rth.
Method #3:
Not in this textbook, but you will find it in other.
Short circuit terminals a-b & do not zero any sources.
RN = Rth = Voc / isc
Works for circuits with or without dependent sources.

## Slide 31
PP 4-11:
Determine the Norton equivalent circuit to the left of terminals a-b.
IN: Calculate isc = IN:
isc
isc
Hence 9 A splitting between two 3  resistors:
IN = 9/2 = 4.5 A
RN: Method #1
Only independent sources: Zero them.
RN = 6//(3+3) = 3 

## Slide 32
PP 4-12:
Determine the Norton equivalent circuit.
IN: Calculate isc = IN:
isc
Observe: SC makes vx = 0 V and hence also 2vx = 0.
isc
6  shorted, hence no current through the 6 :
isc = 10 A
RN: Method #2:
Zero Ind. Sources + Test Source
1 V
(1+2) V
io
KCL @ 1 V node:

## Slide 33
PP 4-12:
Determine the Norton equivalent circuit.
IN: Calculate isc = IN:
isc
isc
RN: Method #3: Rth = Voc/isc
Find Voc=Vab
60 V
Ito current flowing, all elements are now
in series, use Voltage Div to get vx:
Observe: SC makes vx = 0 V and hence also 2vx = 0.
6  shorted, hence no current through the 6 :
isc = 10 A
i
60 V

## Slide 34
Problem 4-51:
Determine the Norton equivalent circuit between terminals a-b.
IN: Calculate isc = IN:
isc
isc
V1
KCL at big node:
KCL at node b:
Method #1: Nodal Analysis

## Slide 35
Problem 4-51:
Determine the Norton equivalent circuit between terminals a-b.
IN: Calculate isc = IN:
Method #2: Source Transformations
isc
20 A
40 V
6//3 = 2 
2 
12 V
isc
All in series:
isc = (40 – 12)/(2+2) = 7 A
isc

## Slide 36
Problem 4-51:
Determine the Norton equivalent circuit between terminals a-b.
RN: Method #1:
Zero Ind. Sources
Rab = 4 // (6//3+2)
= 4 // (2+2)
= 4 // 4
= 2 

## Slide 37
If the entire circuit is replaced by its Thevenin equivalent except for the load, the power delivered to the load is:
The power transfer profile with different RL
For maximum power dissipated in RL, Pmax, for a given RTH and VTH:
Ch. 4 L#5:
4.8 Maximum Power Transfer

## Slide 38
Ex 4-13:
Determine RL for maximum power transfer as well as what Pmax will be.
Method: Determine the Thevenin circuit between a-b. I.e. Vth and Rth.
Rth: Zeroing of sources:
Rth = 6//12 + 3 + 2 = 9  = RL
Vth: Super positioning:
+
Vth1
-
Vth1 = 12 V 12/(6+12) = 8 V
+
Vth2
-
Vth2 = 2A  ((6//12) + 3)
= 2  7 = 14 V
Vth = 8 + 14 = 22V
9 
9 

## Slide 39
PP 4-13:
Determine RL for maximum power transfer as well as what Pmax will be.
Rth: Method #2:
io
V
x4:
Vth:
+
Vth
-
V
vx = -V
vx = 9V

## Slide 40
Problem 4.66:
Determine the maximum power that can be delivered to resistor R.
Rth: Method #1:
Rth = 2 // (3+5)
= 1.6 
+ Vth -
i
i = 60 / 10 = 6 A
Vth = 2i – 10 = 12 – 10 = 2 V