## Slide 1
Chapter 5
Operational Amplifiers
Op Amps
EBN 122 ELECTRICITY AND ELECTRONICS

## Slide 2: Operational Amplifier - Chapter 5
5.2 What is an Op Amp?
5.3 Ideal Op Amp
5.4 Configuration of Op Amp
5.5 Cascaded Op Amp
5.6 Application
  – Digital-to Analog Converter

## Slide 3: 5.2 What is an Op Amp
It is an electronic unit that behaves like a voltage-controlled voltage source.
It is an active circuit element designed to perform mathematical operations of addition, subtraction, multiplication, division, differentiation and integration.
Hence: OPERATIONAL Amplifier

## Slide 4: 5.2 What is an Op Amp Pin Configuration and Circuit Symbol
Transistors, resistors, capacitors, diodes all integrated into an “IC”, integrated circuit.

## Slide 5: 5.2 What is an Op Amp Equivalent Circuit model of a non-ideal Op Amp
Op Amp output:
vo as a function of vd
vd = v2 – v1
vo = Avd = A(v2 –v1)
A = Open-loop voltage gain
Parameter | Range | Ideal
A | 105 – 108 | 
Ri | 105 – 1013  |  
Ro | 10 – 100  | 0 
VCC | 5 – 24 V | 
Typical ranges for op amp parameters
Open-loop: No external feedback from output v0 to input vd
Supply voltage

## Slide 6
5.2 What is an Op Amp A Practical Limitation
Output cannot exceed |VCC|
Linear region where vo = Avd
vd = v2 – v1 = v+ – v-

## Slide 7
PP 5.1 Use a 741 Op Amp with A = 2105, Ri = 2 M, Ro = 50 .
Determine the closed-loop gain vo/vs
Vo
V1
1 V

## Slide 8
Vo
V1
PP 5.1 cont… Use a 741 Op Amp with A = 2105, Ri = 2 M, Ro = 50 .
Determine the closed-loop gain vo/vs.
Nodal analysis:
KCL @ Node V1
KCL @ Node Vo
1
2
1
2

## Slide 9: 5.3 Ideal Op Amp
An ideal op amp has the following characteristics:
  Infinite open-loop gain, A ≈ ∞
  Infinite input resistance, Ri ≈ ∞
  Zero output resistance, Ro ≈ 0
Since Ri = :
i1 = i2 = 0
vd = v2 – v1 = 0
 v2 = v1

## Slide 10
PP 5.1 for ideal opamp Assume vs = 1 V and determine vo and io.
Remember:
i1 = i2 = 0
v+ = v-
v+ = 1 V = v-
i1 = i2 = 0
vd = v2 – v1 = 0
 v2 = v1
1 V
1 V
KCL @ Node v- to get Vo:
KCL @ Node Vo to get io:
9 V

## Slide 11
Problem 5.8 Determine vo for both circuits

## Slide 12
Problem 5.9 Determine vo for both circuits

## Slide 13: Ch. 5 L#2 5.4 Inverting Amplifier
Inverting amplifier reverses the polarity of the input signal while amplifying it
v+ = v- = 0V
KCL at v-

## Slide 14
PP 5.3
Determine the output voltage and current through the feedback resistor.

## Slide 15
Example 5.4
Determine Vo.

## Slide 16
0 V
0 V
v+ = v- = 0V
KCL at v-:
5.4 Inverting Amplifier
Special Case: Current-to-Voltage converter

## Slide 17: 5.5 Non-inverting Amplifier
Non-inverting amplifier is designed to produce positive voltage gain
v+ = v- = Vi
KCL at v-
vi
vi

## Slide 18
5.5 Non-inverting Amplifier
Special Case: Voltage Follower
Output = Input
Advantage: Vi sources a very low current while Vo can source high current. (Remember Op Amp is an Active element getting energy via VCC and –VCC).
Circuit is used a BUFFER to isolate one stage of a circuit from another.

## Slide 19
PP 5.5
Calculate vo.
i+
i+ = 0 A
Because of this, the 3V is divided across the 4 k and 8 k resistors, hence a basic voltage divider.
So:
2 V
2 V
KCL @ v-:

## Slide 20
Problem 5.19
Calculate io.

## Slide 21
Problem 5.25
Calculate vo.

## Slide 22: Ch. 5 L#3 5.6 Summing Amplifier
Summing Amplifier is an op amp circuit that combines several inputs and produces an output that is the weighted sum of the inputs.
Basic configuration of an inverting amplifier but with multiple inputs.

## Slide 23
PP 5-6
Determine vo and io for the following circuit:

## Slide 24: Ch. 5 L#3 5.7 Difference Amplifier
Difference amplifier is a device that amplifies the difference between two inputs but rejects any signals common to the two inputs.
Combination of the inverting and non-inverting op amps.
See derivation from 1st principles in textbook p187 and p188
If R1/R2 = R3/R4: Vo = 0 if V1 = V2
If R2 = R1 and R3 = R4: Vo = V2 – V1

## Slide 25
Example 5.7
Design an Op Amp circuit with inputs v1 and v2 such that vo = -5v1 + 3v2
Design 1: Using only 1 Op Amp
Choose R3 = R4 = 2 k
vo = 3v2 – 5v1

## Slide 26
Example 5.7
Design an Op Amp circuit with inputs v1 and v2 such that vo = -5v1 + 3v2
Design 2: Using 2 Op Amps
Build an inverting amp to obtain va = -3v2.
2. Feed the output va into a summing amplifier along with v1.
va = – 3R3/R3  v2
= – 3v2
vo = – (5R1/R1  v1 + 5R1/5R1  va)
= – 5v1 – va
= – 5v1 – (– 3v2)
= – 5v1 + 3v2

## Slide 27
PP 5-8
Determine io for the following circuit:
Vo

## Slide 28
Ch. 5 L#4 5.8 Cascaded Op Amp Circuits
Total Amplification A = A1A2A3
It is a head-to-tail arrangement of two or more op amp circuits such that the output to one is the input of the next.

## Slide 29
PP 5-9
Determine vo and io.
Voltage Follower or Buffer
Non-Inverter
8 V
8 V
v+ = v- = 8 V
KCL at v-

## Slide 30
PP 5-10
If v1 = 4 V and v2 = 3 V, determine vo.
4 V
3 V

## Slide 31
PP 5-10 (continued)
If v1 = 4 V and v2 = 3 V, determine vo.

## Slide 32
Problem 5-39
Determine v2 such that vo = -16.5 V.

## Slide 33
Problem 5-39
If v1 = 1 V and v2 = 2 V, determine vo.

## Slide 34
Problem 5-59
Determine vo/vs if R = 20 k.