## Slide 1
Chapter 6
Capacitors and Inductors
EBN 111/122 ELECTRICITY AND ELECTRONICS

## Slide 2: Capacitors and Inductors Chapter 6
6.2 Capacitors
6.3 Series and Parallel Capacitors
6.4 Inductors
6.5 Series and Parallel Inductors

## Slide 3: 6.2 Capacitors Physical characteristics
A = Surface are of the metal plate [m2]
 = permittivity of the dielectric [F/m]
d = distance between plates [m]
 = r 0
r = Relative permittivity of material
0 = Permittivity of air (8.854 x 10-12 F/m)
A capacitor is a passive element designed to store energy in its electric field.
A capacitor consists of two conducting plates separated by an insulator (or dielectric).

## Slide 4: 6.2 Capacitors Electrical characteristics
Capacitance C is the ratio of the charge q on one plate of a capacitor to the voltage difference v between the two plates, measured in farads (F).
OR
If i > 0: Capacitor is charging.
If i < 0: Capacitor is discharging.

## Slide 5: 6.2 Capacitors Energy and Power
The energy, w, stored and power p in the capacitor is:
Important characteristics of capacitors:
  It is an open circuit to dc (dv/dt = 0).
  Its voltage cannot change abruptly (dv/dt = ).
  Does not dissipate energy, but stores it when charging or provides it when discharging.

## Slide 6
6.2 Capacitors New Equations
V-I characteristic of a Cap

## Slide 7
PP 6.1 What is the voltage across a 3F capacitor if the charge on one plate is 0.12 mC. How much energy is stored in the capacitor?
PP 6.2 The voltage source connected across a 10 F capacitor is given as:
v(t) = 50 sin 2000t V. Calculate i(t).

## Slide 8
PP 6.3 If the current through a 100 F capacitor is given as:
i(t) = 50 sin (120t) mA, calculate v(1ms) and v(5ms).
Assume v(0) = 0 V
0
1ms

## Slide 9
+ V20 –
+ V30 –
PP 6.5 For DC conditions, calculate the energy stored in the two capacitors.
+ 1V –
+ 3V –
+ 6V –
V30F = 3 V
  w = 0.5Cv2
  = 0.5  3010-6  32
  = 135 J
V20F = (3+6) = 9 V
  w = 0.5Cv2
  = 0.5  2010-6  92
  = 810 J
+ V30 –
+ V20 –

## Slide 10: 6.3 Series and Parallel Capacitors

## Slide 11
PP 6.6 Determine the equivalent capacitance
120 & 60:
  12060 / (120 + 60) = 40 F
40 & 20:
  40 + 20 = 60 F
50 & 70:
  50 + 70 = 120 F
120 & 60:
   Ceq = 40 F
40 F

## Slide 12: Ch. 6 L#2 6.4 Inductors Physical characteristics
An inductor is a passive element designed to store energy in its magnetic field.
An inductor consists of a coil of conducting wire.
Core from iron, steel, plastic or air.
 = permeability = r0

## Slide 13: 6.4 Inductors Electrical characteristics
Important characteristics of inductors:
  It is a short circuit to DC (di/dt = 0).
  Its current cannot change abruptly (di/dt = ).
  Does not dissipate energy, but stores it when charging or provides it when discharging.

## Slide 14
PP 6.8 The current through a 1 mH inductor is i(t) = 20 cos 100t mA. Calculate the voltage and the stored energy.
PP 6.9 The voltage across a 2 H inductor is v(t) = 10(1 – t) V.
Determine the current through the inductor at t = 4 s if i(0) = 2 A.
0
4

## Slide 15
PP 6.10 Determine vC, iL and the energy stored in both the capacitor and the inductor for the DC circuit below.

## Slide 16: 6.4 Series and Parallel Inductors

## Slide 17
Current and voltage relationship for R, L, C
+
+
+

## Slide 18
PP 6.11 Calculate Leq
40+20 = 60
60//30 = 20
20+100 = 120
120//40 = 30
30+20 = 50
50//50 = 25 mH = Leq

## Slide 19
PP 6.12 If i1(t) = 0.6e-2t A and i(0) = 1.4 A ,find
a) i2(0) (b) i2(t) and i(t) (c) v1(t), v2(t) and v(t)
i1(0) = 0.6 A
KCL: i2(0) = i(0) – i1(0)
= 1.4 – 0.6 = 0.8 A

## Slide 20
PP 6.12 continued If i1(t) = 0.6e-2t A and i(0) = 1.4 A ,find
(b) i2(t) and i(t) (c) v1(t), v2(t) and v(t)
i2(0) = 0.8 A
0
t

## Slide 21
PP 6.12 continued … If i1(t) = 0.6e-2t A and i(0) = 1.4 A ,find
(b) i2(t) and i(t) (c) v1(t), v2(t) and v(t)
KCL:
KVL:

## Slide 22
Problem 6.40 The current through a 10 mH inductor is shown below. Determine the voltage across the inductor at t = 1, 3 and 5 ms.
OR

## Slide 23
Problem 6.48 Under steady state dc conditions, find i and v.