## Slide 1
Chapter 2
Basic Laws
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
EBN 111/122 ELECTRICITY AND ELECTRONICS

## Slide 2: Basic Laws - Chapter 2
2.2 Ohm’s Law.
2.3 Nodes, Branches, and Loops.
2.4 Kirchhoff’s Laws.
2.5 Series Resistors and Voltage Division.
2.6 Parallel Resistors and Current Division.
2.7 Wye-Delta Transformations.
L#1
L#2
L#3
L#4

## Slide 3: Chapter 2: Lecture #1 2.2 Ohms Law: V = IR
Ohm’s law states that the voltage V across a resistor is directly proportional to the current I flowing through the resistor.
Resistance R: Physical property of a material to resist the flow of current.

## Slide 4
2.2 Ohms Law: V = IR
Passive Sign Convention
v = + iR
v = iR

## Slide 6
Material | Resistivity (m) | Usage
Copper | 1.72 x 10-8 | Conductor
Gold | 2.45 x 10-8 | Conductor
Carbon | 4 x 10-5 | Semi-conductor
Silicon | 6.4 x 102 | Semi-conductor
Paper | 1 x 1010 | Insulator
Teflon | 3 x 1012 | Insulator
2.2 Ohms Law Resistivity  & Resistance R

## Slide 7
2.2 Ohms Law Resistance R - extremes
R = 0: SHORT Circuit (SC)
v = iR = i  0 = 0
R = ∞: OPEN Circuit (OC)

## Slide 8
Conductance is the ability of an element to conduct electric current; it is the reciprocal of resistance R and is measured in mho’s [ʊ] or siemens [S].
2.2 Ohms Law Conductance G

## Slide 9
2.2 Ohms Law Power dissipated in a Resistor
v=iR
R
i=v/R
MUCHO IMPORTANTE:
Since i2, v2 & R is always ≥0:
P in a resistor is ALWAYS ≥ 0 (positive)

## Slide 10
Example 2-2 In the circuit shown, calculate the current i, the conductance G and the power p.
i= v/R = 30 / 5103 = 6mA
G = 1/R = 1/5000 = 0.2 mS
p = i2R = (610-3 )2  5103
= 180 mW
or:
p = +vi =30  0.006 = 0.18 W
or:
p = v2/R = (30)2 / 5000 = 180mW

## Slide 11
PP 2-2 For the circuit shown, calculate the voltage v, conductance G and power p.
v= iR = 210-3  10103
= 20 V
G = 1/R = 1/10000 = 100 S
p = i2R = (210-3 )2  10103
= 40 mW
or:
p = +vi =20  0.002 = 0.04 W

## Slide 12: 2.3 Nodes, Branches and Loops
A branch represents a single element such as a voltage source or a resistor.
A node is the point of connection between two or more branches.
A loop is any closed path in a circuit.

## Slide 13
2.3 Nodes, Branches and Loops
BRANCHES
“A single element such as a voltage source or a resistor.”
How many branches?
5

## Slide 14
2.3 Nodes, Branches and Loops
NODES
“The point of connection between two or more branches.”
How many nodes?
Node a: 2 Branches
Node b: 4 Branches
Node c: 4 Branches
3

## Slide 15
2.3 Nodes, Branches and Loops
LOOPS
“Any closed path in a circuit.”
How many loops?
6

## Slide 16
2.3 Nodes, Branches and Loops
INDEPENDENT LOOPS
“A loop that contains at least one branch which is not a part of any other independent loop.”
“A loop that cannot be formed by combining / merging any of the other loops.”
Independent sets leads to independent equations

## Slide 17
2.3 Nodes, Branches and Loops
When is it NOT an independent set?
If any loop can be formed by merging any of the other loops.
Dependent set 1:

## Slide 18
Dependent set 2:
2.3 Nodes, Branches and Loops
When is it NOT independent?
If any loop can be formed by merging any of the other loops.

## Slide 19
Dependent set 3:
2.3 Nodes, Branches and Loops
When is it NOT independent?
If any loop can be formed by merging any of the other loops.

## Slide 20
A network with b branches, n nodes, and l independent loops will satisfy the fundamental theorem of network topology:
2.3 Nodes, Branches and Loops
Fundamental theorem of network topology
# branches = # ind-loops + # nodes - 1
5 = 3 + 3 - 1

## Slide 21
2.3 Nodes, Branches and Loops
Series and Parallel
SERIES
Two (2) elements are in series if:
  They exclusively share a single node
   carry the same current.
PARALLEL
Two or more elements are in parallel if:
  They are connected to the same two nodes
   have the same voltage

## Slide 22
PP 2-4 How many branches, nodes and independent loops does the circuit have?
Branches =
Nodes =
Loops =
5
3
3

## Slide 23
Problem 2.5 Find the number of nodes, branches and independent loops.
Branches =
Nodes =
Loops =
15
9
7

## Slide 24
Problem 2.7b Find the number of nodes, branches and independent loops.
Branches =
Nodes =
Loops =
7
5
3

## Slide 25: Chapter 2: Lecture #2 2.4 Kirchhoff’s Laws
Kirchhoff’s current law (KCL) states that the algebraic sum of currents entering and leaving a node (or a closed boundary) is zero.
Mathematically
N = Number of branches connected to the node.
in = nth current entering or leaving.

## Slide 26: 2.4 Kirchhoff’s Laws (KCL) “What goes in, must come out”
i1 +(–i2) + i3 + i4 + (– i5) = 0
Closed Boundary (Super Node):
– i1 – i2 – i3 + i4 + i5 = 0
Entering = Leaving
i1 + i3 + i4 = i2 + i5
Current entering a node: ADD +
Current leaving a node: SUBTRACT –
i1
i2
i3
i4
i5

## Slide 27
2.4 Kirchhoff’s Laws (KCL)
Current Sources in Parallel
IS = I1 + I2 I3
IS = + I1 I2 + I3

## Slide 28
i2
i1
i3
– i1 – i2 + i3 = 0
2.4 Kirchhoff’s Laws (KCL)
Resistive networks

## Slide 29
Kirchhoff’s voltage law (KVL) states that the algebraic sum of all voltages around a closed path (or loop) is zero.
Mathematically,
2.4 Kirchhoff’s Laws (KVL)
“What goes up, must come down”
– v1 + v2 + v3 – v4 + v5 = 0
Convention:
Always go clock wise
In at +: ADD
In at –: SUBTRACT

## Slide 30
VS = V1 V2 V3
2.4 Kirchhoff’s Laws (KVL)
Voltage sources in series

## Slide 31
PP 2-5 Find i, v1 and v2.
i
KVL: – 10 + v1 – 8 – v2 = 0
Ohm: v1 = 4i
Ohm: v2 = – 2i
– 10 + (4i) – 8 – (-2i) = 0
6i = 18
i = 3 A
v1 = 4i = 43 = 12 V
v2 = – 2i = –23 = –6 V
The Test:…
– 10 + v1 – 8 – v2 = 0
– 10 + 12 – 8 – (–6) = – 18 + 18 = 0

## Slide 32
PP 2-7 Find current io and voltage vo.
Observation: Voltage across ALL elements is vo.
KCL: + 6 – io – io/4 – vo/8 = 0
i8 = vo/8 A (ohm’s law)
Ohm: io = vo/2 vo = 2io
+ 6 – io – io/4 – 2io/8 = 0
6 = 1.5io
io = 4 A
vo = 2io = 24 = 8 V
The Test:…
+ 6 – io – io/4 – vo/8 = 0
+ 6 – 4 – 4/4 – 8/8 = 0
6 – 4 – 1 – 1 = 0

## Slide 33
Problem 2-11 Calculate V1 and V2.
1
2
KVL1: – V1 + 1 + 5 = 0
V1 = 6 V
KVL2: + V2 – 5 + 2 = 0
V2 = 3 V
The Test:…
– V1 + 1 + 2 + V2 = 0
– 6 + 1 + 2 + 3 = 0
– 6 + 6 = 0

## Slide 34
Problem 2-18 Determine I and Vab.
KVL1: – 30 + 3I – 10 + 5I + 8 = 0
8I = 32
I = 4 A
+ v3=3I –
+ v5=5I –
1
2
KVL2: – Vab + 5I + 8 = 0
Vab = 5(4) + 8 = 28 V
3
v = + iR
KVL3: – 30 + 3I – 10 + Vab = 0
Vab = 40 – 3(4) = 28 V
Vab

## Slide 35: Chapter 2: Lecture #3 2.5 Series Resistors & Voltage Division
Series: Two or more elements are in series if they are cascaded or connected sequentially and consequently carry the same current.
v1 = iR1 or
v2 = iR2 or
KVL: – v + v1 + v2 = 0
v = v1 + v2
= i(R1 + R2)
= iReq

## Slide 36
2.5 Series Resistors & Voltage Division
VOLTAGE DIVISION
v1 = iR1
v2 = iR2
Substitute i into v1 and v2:

## Slide 37
2.5 Series Resistors & Voltage Division
Req for more than 2 R’s
R1
R2
R3
RN
v
+ v1 –
+ v2 –
+ v3 –
+ vN –

## Slide 38
2.5 Series Resistors & Voltage Division
Req for more than 2 R’s
R1
R2
R3
R4
R5
R6
R7
v
+
v4
–
??
??

## Slide 39: 2.6 Parallel Resistors & Current Division
Parallel: Two or more elements are in parallel if they are connected to the same two nodes and consequently have the same voltage across them.
KCL: i – i1 – i2 = 0
i = i1 + i2
Substitute i1 and i2 into KCL:
i1 = v/R1
v = i1R1 = i2R2
i2 = v/R2
Ohm:

## Slide 40
2.6 Parallel Resistors & Current Division
Req for 2 R’s
For TWO // resistors:

## Slide 41
2.6 Parallel Resistors & Current Division
Req for more than 2 R’s
R1
R2
R3
RN
Then does it mean that:
If
NO!

## Slide 42
2.6 Parallel Resistors & Current Division
Current Division
v = i1R1 = i2R2
Substituting v:
Ohm:
Ito i2:

## Slide 43
2.6 Parallel Resistors & Current Division
Current Division – more than 2 R’s
G1
G2
G3
GN

## Slide 44
2.6 Parallel Resistors & Current Division
Voltage Division - Summary
+
_
V1
+
_
V2
+
_
V
+
_
V1
+
_
V2
+
_
V3
+
_
V
R1
R2
R3
R1
R2

## Slide 45
2.6 Parallel Resistors & Current Division
Current Division - Summary
i1
i2
i1
i2
i2
i
i
R3
R1
R2
R1
R2

## Slide 46
PP 2-9 Determine Req

## Slide 47
PP 2-12 Find v1 an v2 in the circuit. Also calculate i1 and i2 and the power dissipated in the 12  and 40  resistors.

## Slide 48
Problem 2-31 Determine i1 to i5 .

## Slide 49: Chapter 2: Lecture #4 2.7 Wye-Delta Transformations WYE / Y or T or Star Network

## Slide 50: 2.7 Wye-Delta Transformations Δ or  Network
Δ


## Slide 51: 2.7 Wye-Delta Transformations Y inside a Δ
Delta Δ: Ra, Rb, Rc.
Name the nodes a, b, and c.
Ra is opposite node a
Rb is opposite node b
Rc is opposite node c
Ra
Rc
Rb

## Slide 52: 2.7 Wye-Delta Transformations Y inside a Δ
Delta Y: R1, R2, R3.
Name the nodes a, b, and c.
R1 is connected to node a
R2 is connected to node b
R3 is connected to node c
R2
R1
R3

## Slide 53: 2.7 Wye-Delta Transformations Y inside a Δ
Delta ⟶ Wye
Wye ⟶ Delta
Δ
Y
⟵
Δ
Y
⟵
Product of adjacent Δ R’s
All possible pro-ducts of Y R’s 2@t

## Slide 54
2.7 Wye-Delta Transformations Special Case: Balanced Y and Δ
Ra = Rb = Rc = RΔ
and
R1 = R2 = R3 = RY
then:

## Slide 55
Problem 2-48 Convert the circuits from Y to Δ :

## Slide 56
Problem 2-49 Convert the circuits from Δ to Y :

## Slide 57
Problem 2-44 Determine Req between terminals a and b :

## Slide 58
Chapter 2: Lecture #5 Additional Problems
Problem 2-17 Determine v1, v2 and v3 in the circuit.

## Slide 59
Problem 2-32 Determine i1, i2, i3 and i4 in the circuit.

## Slide 60
Problem 2-37 Find R for the circuit.

## Slide 61
Problem 2-55 Calculate Io in the circuit.