## Slide 1
Chapter 3
Methods of Analysis
EBN 111/122 ELECTRICITY AND ELECTRONICS

## Slide 2: Methods of Analysis - Chapter 3
3.1 Motivation
3.2 Nodal analysis.
3.3 Nodal analysis with voltage sources.
3.4 Mesh analysis.
3.5 Mesh analysis with current sources.
3.6 Nodal and mesh analysis by inspection.
3.7 Nodal versus mesh analysis.

## Slide 3
What are the things which we need to know in order to determine the answers?
3.1 Motivation (1)
If you are given the following circuit, how can we determine (1) the voltage across each resistor, (2) current through each resistor. (3) power generated by each current source, etc.

## Slide 4: Things we need to know in solving any resistive circuit with current and voltage sources only:
How should we apply these laws to determine the answers?
Kirchhoff’s Current Laws (KCL)
Kirchhoff’s Voltage Laws (KVL)
Ohm’s Law
3.1 Motivation (2)
The LAWS

## Slide 5
KCL ⟶ Nodal Analysis
aka (Voltage Node Analysis)
KVL ⟶ Mesh (Current) Analysis
3.1 Motivation (3)
THESE TWO TECHNIQUES
Can be used in any linear circuit
To obtain a set of simultaneous equations
Equations solved using:
  Substitution
  Cramer’s rule (Appendix A)

## Slide 6: 3.2 Nodal Analysis Why?
It provides a general procedure for analyzing circuits using node voltages as opposed to element voltages as the circuit variables.
Reduces the number of equations required to solve a circuit.

## Slide 7: 3.2 Nodal Analysis STEPS
Steps to determine the node voltages:
Select a node as the reference node (ground).
Assign voltages V1,V2,…,Vn-1 to the remaining “critical” nodes.
  “Critical node” = node with more than 2 branches attached.
  The voltages are referenced with respect to the reference node. I.e. Measured between Node and Ground.
Apply KCL to each of the non-reference nodes. Use Ohm’s law to express the branch currents in terms of node voltages.
Solve the resulting simultaneous equations to obtain the unknown node voltages.

## Slide 8
STEP 1: Select a Reference Node
WHERE??
    Negative terminal of V-source
    Entry terminal of I-source
    Node with many branches
    Bottom node (many cases)
STEP 1
V1
V2
STEP 2
STEP 2: Name critical nodes: V1, V2, …, Vn
3.2 Nodal Analysis
EXAMPLE 1

## Slide 9
V1
V2
STEP 3: Apply KCL to each node
3.2 Nodal Analysis
EXAMPLE 1
Assign a current to each branch at each critical node.
All currents to point OUT of the node.
Remember: Current flows from HIGH to LOW voltage 
All branch currents to be written ito Ohm’s law:
Number of critical nodes = number of equations.
Number of branches = number of terms.

## Slide 10
V1
V2
STEP 3: Apply KCL to each node
3.2 Nodal Analysis
EXAMPLE 1
Node 1 (4 Branches):
Node 2 (3 Branches):
Negative because outgoing branch current is opposite to the source’s current
Flows from? V2
Flows to? Gnd
Flows through? R3
V2
V1
R2

## Slide 11
3.2 Nodal Analysis
EXAMPLE 2
Node 1:
x6
Write ito:
1
Node 2:
x42
2
1
2
V1
V2
Write ito:
a1 = 4
b1 = -1
a2 = -7
b2 = 13

## Slide 12
3.2 Nodal Analysis
Ex. 2 – Method 1: Elimination
1
2
V1
V2
From :
1
3
3
in :
2
From :
3

## Slide 13
3.2 Nodal Analysis
Ex. 2 – Method 2: Cramer’s Rule
See Appendix A
1
2

## Slide 14
PP 3-2 Determine the node voltages.
V1
V2
V3
Node 1:
x6
1
Node 2:
x12
2
Node 3:
x6
3

## Slide 15
PP 3-2 continued: Calculating 
+
+
+
-
-
-

## Slide 16
PP 3-2 continued: Calculating 1
+
+
+
-
-
-

## Slide 17
PP 3-2 continued: Calculating 2
+
+
+
-
-
-

## Slide 18
PP 3-2 continued: Calculating 3
+
+
+
-
-
-
0

## Slide 19
Ch. 3 L#2: 3.3 Nodal Analysis With Voltage sources
10.00
5.00
Case 1: Vs between a node and GND:
V1 – 0 = 10 V
V1
V2
V3
Case 2: Vs between two nodes:
V2 – V3 = 5 V
SUPERNODE

## Slide 20
3.3 Nodal Analysis With Voltage sources
V1
V2
V3
1
2
Solve for V2 and V3 from and
3
2
3
SUPERNODE
Formed by enclosing a (dependent or independent) voltage source connected between two non-reference nodes along with any elements connected in parallel with that voltage source.

## Slide 21
PP 3-3 Find v and i in the circuit.

## Slide 22
PP 3-3 Continued…
PP 3-3 Find v and i in the circuit.

## Slide 23
PP 3-4 Find v1, v2, v3 and i.

## Slide 24
PP 3-4 Continued…

## Slide 25
Problem 3-16 Find v1, v2 and v3.

## Slide 26
Problem 3-4 Find I1 through I4.
V1
V2

## Slide 27: Ch. 3 L#3: 3.4 Mesh Analysis Why?
  Mesh analysis provides another general procedure for analyzing circuits using mesh currents as the circuit variables.
  Nodal analysis applies KCL to find unknown voltages in a given circuit, while mesh analysis applies KVL to find unknown currents.
  A mesh is a loop which does not contain any other loops within it.

## Slide 28: 3.4 Mesh Analysis STEPS
Steps to determine the mesh currents:
  Assign mesh currents i1, i2, …, in to the n meshes – clock wise.
  Apply KVL to each of the n meshes. Use Ohm’s law to express the voltages in terms of the mesh currents.
  Solve the resulting n simultaneous equations to get the mesh currents.
I1 = i1
I2 = i2
I3 = i1 – i2

## Slide 29
3.4 Mesh Analysis STEPS: KVL in Loops
– V1 + R1i1 + R3(i1 – i2) = 0
+
i1R3
–
–
i2R3
+
R3 has 2 currents flowing through it: i1 and i2
i2 causes a voltage drop from bottom to top: i2R3
i1 causes a voltage drop from top to bottom: i1R3
a1i1 + b1i2 = k1
Loop 1:
Loop 2:
V2 + R3(i2 – i1) + i2R2 = 0
(–R3)i1 + (R2 + R3) i2 = – V2
+ i1R1 –
+ i2R2 –
Write ito:
(R1+ R3)i1 + (–R3) i2 = V1
a2i1 + b2i2 = k2
Write ito:
Inet through R3 wrt loop 1
Inet through R3 wrt loop 2
R(iloop – iopposing_loop)

## Slide 30
PP 3-5
Determine i1 and i2.
i1
i2
– 36 + 2i1 + 12(i1 – i2) + 4i1 = 0
Loop 1:
(2+12+4)i1 + (–12)i2 = 36
(18)i1 + (–12)i2 = 36
1
2
Loop 2:
(–12)i1 + (3+12+9)i2 = –24
(–12)i1 + (24)i2 = –24
24 + 3i2 + 12(i2 – i1) + 9i2 = 0
Matrix:
= 288

## Slide 31
PP 3-6 Determine Io.
i1
i2
i3
Note:
Io = i3
CCVS: 10io = 10i3
– 20 + 4(i1 – i3) + 2(i1 – i2) = 0
Loop 1:
(4+2)i1 + (–2)i2 + (–4)i3 = 20
6i1 + (–2)i2 + (–4)i3 = 20
1
– 10i3 + 2(i2 – i1) + 8(i2 – i3) = 0
Loop 2:
(-2)i1 + (10)i2 + (–18)i3 = 0
6i3 + 8(i3 – i2) + 4(i3 – i1) = 0
Loop 3:
(-4)i1 + (-8)i2 + (18)i3 = 0
2
3

## Slide 32
PP 3-6 Determine Io cont. …
+
+
+
-
-
-
i1
i2
i3
+
+
+
-
-
-

## Slide 33
Problem 3-39 Determine i1 and i2 (Mesh Analysis)
i1
i2
Note:
Ix = i1- i2
CCVS: 2Ix = 2(i1- i2)
– 10 + 4i1 – 2(i1 – i2) + 6(i1 – i2 ) = 0
Loop 1:
8i1 + (–4)i2 = 10
12 + 6(i2 – i1 ) + 2i2 = 0
Loop 2:
(-6)i1 + 8i2 = -12
1
2
+ 2 :
2
1
(-6+16)i1 + (8-8)i2 = (-12+20)
i1 = 0.8 A
10i1 + 0i2 = 8
3
in :
3
2
(-6)0.8 + 8i2 = -12
i2 = -0.9 A

## Slide 34
Problem 3-39 Determine i1 and i2 (Supernode)
Note:
Supernode: V1 – V2 = 2Ix
Two const. Voltage nodes
Ix = V1/6
KCL @ SN:
10 V
12 V
x12
V2
V1
Supernode:
x3
1
2
+ :
1
2
i1
i2

## Slide 35
Problem 3-39 Determine i1 and i2 (Node Voltage)
Note:
Only 1 critical node
Const. Voltage nodes
Ix = V1/6
V over 4 
V1
Node 1:
V1 – 2Ix
10 V
12 V
x12
i1
i2

## Slide 36
Ch. 3 L#4: 3.5 Mesh Analysis With Current Sources
CASE #1: A current source exists only in one mesh: That loop current is then known.
i2 = -5 A
-10 + 4i1 + 6(i1 – i2) = 0
-10 + 10i1 – 6(-5) = 0
10i1 = -20
i1 = -2 A

## Slide 37
3.5 Mesh Analysis With Current Sources
A SUPERMESH results when two meshes have a current source (dependent or independent), with or without other elements in series, in common.
i2 – i1 = 6
i1 = i2 – 6
-20 + 6i1 + 10i2 + 4i2 = 0
CASE #2: A current source exists between two meshes: SUPERMESH
Common source:
Note: i2 flows in the same direction as the source.
SUPERMESH:
1
2
1
2
in
-20 + 6(i2 – 6) + 10i2 + 4i2 = 0
i2 = 2.8 A
i1 = - 3.2 A

## Slide 38
PP 3-7 Determine i1, i2 and i3.
i1 – i2 = 3
Common source:
Supermesh:
-6 + 2(i1 – i3) + 4(i2 – i3) + 8i2 = 0
2i1 + 12i2 – 6i3 = 6
Loop 3:
2(i3 – i1) + 2i3 + 4(i3 – i2) = 0
-2i1 – 4i2 + 8i3 = 0
1
2
3

## Slide 39
Problem 3-46
Solve for the mesh currents.
i4 = 2 A
Loop 1:
-60 + 2i1 + 1(i1 – i2) = 0
3i1 – i2 = 60
Loop 2:
1(i2 – i1) + 3(i2 – 2) + 1(i2 – i3) = 0
– i1 + 5i2 – i3 = 6
Loop 3:
1(i3 – i2) + 10i3 = 0
–i2 + 11i3 = 0

## Slide 40
Problem 3-46
Find v0 and io
i3
-i1 + i2 = 2io
Common source:
Supermesh:
2i1+ 1(i1 – i3) + 2(i2 – i3) + 16 = 0
3i1 + 2i2 – 3i3 = -16
Loop 3:
1(i3 – i1) + 3i3 + 2(i3 – i2) = 0
-i1 – 2i2 + 6i3 = 0
i1
i2
Since: i1 = -io
i1 + i2 = 0
1
2
3
vo:
KVL: 2i1+ 1(i1 – i3) + vo = 0
vo = -3i1 + i3
i1= -10.67 A
i2 = 10.67 A
i3 = 1.78 A
vo = 33.78 V

## Slide 41
Ch. 3 L#5: 3.6 Nodal and Mesh Analysis by inspection Special case #1: All sources = independent current sources
Conductance Matrix
- Diagonal elements (G11, G22, …) = sum of all G’s connected to that node.
- Off-diagonal elements = –G connected between the two nodes.
1
2
1
2
Sum of the currents entering the node:
In = +
Out = –

## Slide 42
3.6 Nodal and Mesh Analysis by inspection Special case #2: All sources = independent voltage sources
Resistance Matrix
- Diagonal elements (R11, R22, …) = sum of all R’s in the loop.
- Off-diagonal elements = –R common to two loop between the two nodes
1
2
1
2
Sum of all the voltage increases in the loop:
In @ – = +
In @ + = –
Remember: V is taken to the other side in the KVL equation.

## Slide 43
PP 3-8 By inspection, obtain the node voltage equations for the circuit in matrix form.
.
0.1
1 S
0.2
0.25
0.5

## Slide 44
PP 3-9 By inspection, obtain the mesh-current equations for the circuit in matrix form.

## Slide 45
Problem 3-69 By inspection, obtain the node voltage equations for the circuit

## Slide 46: 3.7 Nodal versus Mesh Analysis (1)
To select the method that results in the smaller number of equations. For example:
Choose nodal analysis for circuit with fewer nodes than meshes.
  *Choose mesh analysis for circuit with fewer meshes than nodes.
  *Networks that contain many series connected elements, voltage sources, or supermeshes are more suitable for mesh analysis.
  *Networks with parallel-connected elements, current sources, or supernodes are more suitable for nodal analysis.
If node voltages are required, it may be expedient to apply nodal analysis. If branch or mesh currents are required, it may be better to use mesh analysis.

## Slide 47
Ch. 3 L#6:
3.9 Transistor Circuits
BJT = Bipolar Junction Transistor
npn transistor
Collector = C
Emitter = E
Base
B
C
E
B
Currents
IE
IC
IB
KCL: IE = IC + IB
C
E
B
– VCB +
+ VBE –
+
VCE
–
Voltages
KVL: VCE = VBE + VCB
VBE = 0.7 V

## Slide 48
3.9 Transistor Circuits
Currents
C
E
B
IE
IC
IB
KCL: IE = IC + IB
IC = IB
 IE = (1+)IB
 ranges between 50 ⟶ 100
 = “Common-emitter current gain”
IC = IE
ranges between
0.98 ⟶ 0.999
 = “Common-base current gain”

## Slide 49
3.9 Transistor Circuits
Equivalent network model
C
E
B
IE
IC
IB
C
E
B
IE
IC
IB
+
VCE
–
+
VBE = 0.7 V
–
A transistor is equivalent to a
current controlled current source.
IB
How does one analyse a circuit with a transistor in it?
Method #1: Mesh Analysis
Method #2: Node Analysis
Only applicable if the equivalent network model is used.

## Slide 50
PP 3-12 Determine vo and VCE for the transistor circuit in which VBE = 0.7 V and  = 100. METHOD #1
IC = IB
IB
IE = (1+)IB
In
Out
KVL for Input Loop:
-5 + 10000IB + 0.7 + 200IE = 0
VBE =
1
2
KVL for Output Loop:
- 200IE – VCE – 500IC + 12 = 0
Note:
IC = IB
v0 = 200  IE = 200  (1+)IB
The Method:
Write loop equations ito currents IB, IE and IC.
Use IE = (1+)IB and IC = IB to write all ito IB.
Solve for IB from Input loop.
Solve for VCE from Output loop.

## Slide 51
PP 3-12 continued…
From solve for:
-vo – VCE – 500IC + 12 = 0
-[200  (1+)IB] – VCE – 500IB + 12 = 0
VCE = 12 – 20200IB – 50000IB
= 12 – 70200  IB
= 2 V
2
IC = IB
IB
IE = (1+)IB
In
Out
From solve for IB:
-5 + 10000IB + 0.7 + 200(1+100)IB = 0
30200  IB = 4.3
IB = 0.1424 mA
1
Hence:
v0 = 200  (1+100)IB
= 200  1010.14210-3
= 2.87 V

## Slide 52
PP 3-13 Determine vo and Io for the transistor circuit in which VBE = 0.7 V and  = 80.
METHOD #2 – Node Analysis
Note:
E is connected to GND @ 0 V
VCE = VC – VE = VC – 0 = VC = vo
Io = vo / 20k
VBE = VB – VE = 0.7 – 0 = 0.7 V
1 V and 10 V sources connected to GND
IB = (1 – 0.7) / 120k = 2.5 A
C
E
B

## Slide 53
PP 3-13 continued… METHOD #2 – Node Analysis
KCL at Collector (C):

## Slide 54
Problem 3-89 Determine VCE and IB for the transistor circuit in which VBE = 0.7 V and  = 100.
C
E
B
Note:
E @ 0 V
VBE = VB = 0.7 V
+
0.7 V
–
Out
In
+
VCE
–
IC = IB
KVL for Input Loop:
–3 – 0.7 + 100kIB + 0.7 = 0
IB = 3 / 100k
= 30 A
KVL for Output Loop:
–VCE +15 – 1000IC = 0
VCE = 15 – 1000(10030)
= 12 V
IB
–
V
+